## Slide 1
Lead service line need is not one problem
1
States face different mixes of identification and replacement work
Where are infrastructure needs greatest across U.S. states?
01 IDENTIFY
Resolve Lead Status Unknown lines
Identification Need
= Lead Status Unknown
02 REPLACE
Act on known Lead and GRR lines
Known Replacement Inventory
= Lead + GRR
Comparing states on only one measure would hide where their actual workload sits.
Scope: 43,993 complete-report Community Water Systems across 50 states and DC
Notes: Source: U.S. EPA 2026 Q2 Service Line Inventory. Analytical source: completed Lead_Service_Line_Analysis.ipynb and outputs/state_service_line_summary.csv. Known Replacement Inventory = Lead + GRR. Identification Need = Lead Status Unknown, not confirmed lead. Complete-report Community Water Systems only. No composite ranking. Population comparisons use 2025 Census state resident population for the 2026 Q2 inventory.

## Slide 2
Most of the reported national workload
is still unresolved identification
2
National inventory within the analytical sample
Lead Status Unknown
21.59M
Chart: 
| Service lines
Unknown | 21589524
Known replacement | 3115308
Known Replacement Inventory
3.12M
2.18M Lead + 0.94M GRR
6.9×
as many Unknown lines as lines already classified for replacement
Unknown lines require identification.
They are not confirmed lead lines.
Source: U.S. EPA 2026 Q2 Service Line Inventory. Counts reflect the analytical sample.
Notes: Source: U.S. EPA 2026 Q2 Service Line Inventory. Analytical source: completed Lead_Service_Line_Analysis.ipynb and outputs/state_service_line_summary.csv. Known Replacement Inventory = Lead + GRR. Identification Need = Lead Status Unknown, not confirmed lead. Complete-report Community Water Systems only. No composite ranking. Population comparisons use 2025 Census state resident population for the 2026 Q2 inventory.

## Slide 3
The same national challenge looks very different
from state to state
3
Known Replacement Inventory
Lead Status Unknown
Replacement-
heavy
Illinois
Chart: 
| Illinois
Known Replacement | 672210
Unknown | 529706
672,210
529,706
Largest already-classified replacement inventory
Identification-
heavy
Texas
Chart: 
| Texas
Known Replacement | 114501
Unknown | 2178881
114,501
2,178,881
Pennsylvania
Chart: 
| Pennsylvania
Known Replacement | 113717
Unknown | 2055512
113,717
2,055,512
Much larger unresolved identification inventories
Substantial work
on both dimensions
Ohio
Chart: 
| Ohio
Known Replacement | 321502
Unknown | 878788
321,502
878,788
New York
Chart: 
| New York
Known Replacement | 289055
Unknown | 951163
289,055
951,163
Source: U.S. EPA 2026 Q2 Service Line Inventory. Narrative examples, not statistical clusters. All bars use the same scale.
Notes: Source: U.S. EPA 2026 Q2 Service Line Inventory. Analytical source: completed Lead_Service_Line_Analysis.ipynb and outputs/state_service_line_summary.csv. Known Replacement Inventory = Lead + GRR. Identification Need = Lead Status Unknown, not confirmed lead. Complete-report Community Water Systems only. No composite ranking. Population comparisons use 2025 Census state resident population for the 2026 Q2 inventory.

## Slide 4
Chart: Known Replacement Inventory
| 69230.000000 | 16.000000 | 2812.000000 | 11569.000000 | 12839.000000 | 21412.000000 | 13171.000000 | 6292.000000 | 17155.000000 | 44559.000000 | 50342.000000 | 490.000000 | 2769.000000 | 190947.000000 | 67950.000000 | 26807.000000 | 28036.000000 | 20558.000000 | 1599.000000 | 3136.000000 | 41737.000000 | 255524.000000 | 87183.000000 | 23670.000000 | 70968.000000 | 3220.000000 | 48712.000000 | 1091.000000 | 260.000000 | 135360.000000 | 331.000000 | 12934.000000 | 5658.000000 | 14244.000000 | 0.000000 | 31489.000000 | 19245.000000 | 2697.000000 | 64134.000000 | 898.000000 | 1910.000000 | 13819.000000 | 6922.000000 | 8398.000000 | 158815.000000 | 3415.000000
Other states | 192502 | 25945 | 704381 | 477926 | 599523 | 141284 | 281092 | 113360 | 13427 | 1665928 | 630117 | 34235 | 96673 | 545507 | 180539 | 106076 | 424074 | 719101 | 41662 | 563397 | 349967 | 301508 | 209216 | 161821 | 895013 | 65847 | 88447 | 128987 | 3041 | 860857 | 327310 | 798785 | 97950 | 623329 | 27093 | 55695 | 348969 | 96462 | 621686 | 95149 | 36284 | 529417 | 220180 | 232026 | 182814 | 80872
Illinois | 529706
Identification examples | 2178881 | 2055512
High on both | 878788 | 951163
A single ranking would hide
where each state’s workload sits
4
Texas
Pennsylvania
New York
Ohio
Illinois
What this reveals
Replacement and identification needs do not consistently move together.
One overall “need” ranking would hide these differences.
Planning should distinguish known replacement work from inventory still requiring identification.
This pattern describes inventory. It does not measure progress, maturity, or cause.
Source: U.S. EPA 2026 Q2 Service Line Inventory. Each point represents one state or DC.
Notes: Source: U.S. EPA 2026 Q2 Service Line Inventory. Analytical source: completed Lead_Service_Line_Analysis.ipynb and outputs/state_service_line_summary.csv. Known Replacement Inventory = Lead + GRR. Identification Need = Lead Status Unknown, not confirmed lead. Complete-report Community Water Systems only. No composite ranking. Population comparisons use 2025 Census state resident population for the 2026 Q2 inventory.

## Slide 5
State size changes who stands out,
and local evidence is needed before acting
Absolute workload
Raw totals show where the largest overall inventories are concentrated.
Relative scale
Per 10,000 state residents
Raw top 10 retained after normalization
6 of 10
Known Replacement
3 of 10
Identification Need
Illinois: #1 Known Replacement
Pennsylvania: #1 Unknown
Both per 10,000 state residents
Rhode Island, Louisiana and New Mexico become more visible.
Decision implication
State inventories can guide deeper local investigation.
Intervention decisions require utility-level records, GIS information, inspections, funding information, local capacity, project plans and other local evidence.
Next question
How do state and utility identification and replacement needs align with available funding
and local capacity to complete service-line replacement?
Unknown does not mean lead. Inventory does not measure exposure or water quality. Incomplete-report systems are excluded.
Sources: U.S. EPA 2026 Q2 Service Line Inventory; U.S. Census Bureau 2025 resident population estimates (population context).
5
Notes: Source: U.S. EPA 2026 Q2 Service Line Inventory. Analytical source: completed Lead_Service_Line_Analysis.ipynb and outputs/state_service_line_summary.csv. Known Replacement Inventory = Lead + GRR. Identification Need = Lead Status Unknown, not confirmed lead. Complete-report Community Water Systems only. No composite ranking. Population comparisons use 2025 Census state resident population for the 2026 Q2 inventory.