## Slide 1
Lead service line need is not one problem
1
States face different mixes of identification and replacement work
Where are infrastructure needs greatest across U.S. states?
01 IDENTIFY
Resolve Lead Status Unknown lines
Identification Need
= Lead Status Unknown
02 REPLACE
Act on known Lead and GRR lines
Known Replacement Inventory
= Lead + GRR
Comparing states on only one measure would hide where their actual workload sits.
Scope: 43,993 complete-report Community Water Systems across 50 states and DC
Notes: Source: U.S. EPA 2026 Q2 Service Line Inventory. Analytical source: completed Lead_Service_Line_Analysis.ipynb and outputs/state_service_line_summary.csv. Known Replacement Inventory = Lead + GRR. Identification Need = Lead Status Unknown, not confirmed lead. Complete-report Community Water Systems only. No composite ranking. Population comparisons use 2025 Census state resident population for the 2026 Q2 inventory.

## Slide 2
Most of the reported national workload
is still unresolved identification
2
National inventory within the analytical sample
Lead Status Unknown
21.59M
Chart: 
| Service lines
Unknown | 21589524
Known replacement | 3115308
Known Replacement Inventory
3.12M
2.18M Lead + 0.94M GRR
6.9×
as many Unknown lines as lines already classified for replacement
Unknown lines require identification.
They are not confirmed lead lines.
Source: U.S. EPA 2026 Q2 Service Line Inventory. Counts reflect the analytical sample.
Notes: Source: U.S. EPA 2026 Q2 Service Line Inventory. Analytical source: completed Lead_Service_Line_Analysis.ipynb and outputs/state_service_line_summary.csv. Known Replacement Inventory = Lead + GRR. Identification Need = Lead Status Unknown, not confirmed lead. Complete-report Community Water Systems only. No composite ranking. Population comparisons use 2025 Census state resident population for the 2026 Q2 inventory.

## Slide 3
The same national challenge looks very different
from state to state
3
Known Replacement Inventory
Lead Status Unknown
Replacement-
heavy
Illinois
Chart: 
| Illinois
Known Replacement | 672210
Unknown | 529706
672,210
529,706
Largest already-classified replacement inventory
Identification-
heavy
Texas
Chart: 
| Texas
Known Replacement | 114501
Unknown | 2178881
114,501
2,178,881
Pennsylvania
Chart: 
| Pennsylvania
Known Replacement | 113717
Unknown | 2055512
113,717
2,055,512
Much larger unresolved identification inventories
Substantial work
on both dimensions
Ohio
Chart: 
| Ohio
Known Replacement | 321502
Unknown | 878788
321,502
878,788
New York
Chart: 
| New York
Known Replacement | 289055
Unknown | 951163
289,055
951,163
Source: U.S. EPA 2026 Q2 Service Line Inventory. Narrative examples, not statistical clusters. All bars use the same scale.
Notes: Source: U.S. EPA 2026 Q2 Service Line Inventory. Analytical source: completed Lead_Service_Line_Analysis.ipynb and outputs/state_service_line_summary.csv. Known Replacement Inventory = Lead + GRR. Identification Need = Lead Status Unknown, not confirmed lead. Complete-report Community Water Systems only. No composite ranking. Population comparisons use 2025 Census state resident population for the 2026 Q2 inventory.

## Slide 4
Chart: Known Replacement Inventory
| 69230.000000 | 16.000000 | 2812.000000 | 11569.000000 | 12839.000000 | 21412.000000 | 13171.000000 | 6292.000000 | 17155.000000 | 44559.000000 | 50342.000000 | 490.000000 | 2769.000000 | 190947.000000 | 67950.000000 | 26807.000000 | 28036.000000 | 20558.000000 | 1599.000000 | 3136.000000 | 41737.000000 | 255524.000000 | 87183.000000 | 23670.000000 | 70968.000000 | 3220.000000 | 48712.000000 | 1091.000000 | 260.000000 | 135360.000000 | 331.000000 | 12934.000000 | 5658.000000 | 14244.000000 | 0.000000 | 31489.000000 | 19245.000000 | 2697.000000 | 64134.000000 | 898.000000 | 1910.000000 | 13819.000000 | 6922.000000 | 8398.000000 | 158815.000000 | 3415.000000
Other states | 192502 | 25945 | 704381 | 477926 | 599523 | 141284 | 281092 | 113360 | 13427 | 1665928 | 630117 | 34235 | 96673 | 545507 | 180539 | 106076 | 424074 | 719101 | 41662 | 563397 | 349967 | 301508 | 209216 | 161821 | 895013 | 65847 | 88447 | 128987 | 3041 | 860857 | 327310 | 798785 | 97950 | 623329 | 27093 | 55695 | 348969 | 96462 | 621686 | 95149 | 36284 | 529417 | 220180 | 232026 | 182814 | 80872
Illinois | 529706
Identification examples | 2178881 | 2055512
High on both | 878788 | 951163
A single ranking would hide
where each state’s workload sits
4
Texas
Pennsylvania
New York
Ohio
Illinois
Source: U.S. EPA 2026 Q2 Service Line Inventory. Each point represents one state or DC.
WHAT THIS REVEALS
For Unknown lines, identification is the gating step.
An Unknown line must be classified before its replacement need can be determined.
Known Lead + GRR lines can already move toward replacement planning.
Nationally, Unknown inventory is 6.9× the known replacement inventory.
Identification Need is larger in 49 of 51 states/DC.
This describes reported inventory, not project progress or implementation capacity.
Notes: Source: U.S. EPA 2026 Q2 Service Line Inventory. Analytical source: completed Lead_Service_Line_Analysis.ipynb and outputs/state_service_line_summary.csv. Known Replacement Inventory = Lead + GRR. Identification Need = Lead Status Unknown, not confirmed lead. Complete-report Community Water Systems only. No composite ranking. Population comparisons use 2025 Census state resident population for the 2026 Q2 inventory.

## Slide 5
Closing the identification gap is the broadest challenge
Local evidence determines what happens next
Decision implication
The more Unknown lines are classified,
the clearer the replacement workload becomes.
Why population context matters
Raw totals show absolute workload and tend to favor larger states.
Per 10,000 state residents shows inventory scale relative to state population.
These rates do not measure affected residents, customers, exposure, or prevalence.
Raw top 10 retained in the population-adjusted top 10
6 of 10
Known Replacement
3 of 10
Identification Need
Illinois: #1 Known Replacement
Pennsylvania: #1 Unknown
Both per 10,000 state residents
Next question
Once service lines are identified, which utility-level, geographic, funding, and local-capacity factors determine where replacement can move forward?
Unknown does not mean lead. Inventory does not measure exposure or water quality. Incomplete-report systems are excluded.
Sources: U.S. EPA 2026 Q2 inventory data; 2025 Census resident population estimates (population context).
5
Notes: Source: U.S. EPA 2026 Q2 Service Line Inventory. Analytical source: completed Lead_Service_Line_Analysis.ipynb and outputs/state_service_line_summary.csv. Known Replacement Inventory = Lead + GRR. Identification Need = Lead Status Unknown, not confirmed lead. Complete-report Community Water Systems only. No composite ranking. Population comparisons use 2025 Census state resident population for the 2026 Q2 inventory.